MATLAB Routines – ODEs

ODEProb – routines for Taylor Methods, solving a couple of examples.

Freefall –

h0=100;

tmax=5;

tmin=0;

[t,y]=ode45('odef',[tmin tmax],[h0;0]);

plot(t,y(:,1),'k')

hold on

[t,y]=ode45('gravf',[tmin tmax],[h0;0]);

plot(t,y(:,1),'r.')

hold off

| function dy=odef(t,y); dy(1,1)=y(2); dy(2,1)=-9.8; | function dy=gravf(t,y); G=6.67E-11; M=5.97E24; R=6375000; dy(1,1)=y(2); dy(2,1)=-G*M/(R+y(1)).^2; |
| --- | --- |

freefall1 (uses saveeps)

Damped Freefall

h0=100;

tmax=5;

tmin=0;

[t,y]=ode45('odef',[tmin tmax],[h0;0]);

plot(t,y(:,1),'k')

hold on

[t,y]=ode45('gravf',[tmin tmax],[h0;0]);

plot(t,y(:,1),'r.')

[t,y]=ode45('dgravf',[tmin tmax],[h0;0]);

plot(t,y(:,1),'b--')

hold off

| function dy=gravf(t,y); G=6.67E-11; M=5.97E24; R=6375000; m=90; C=.8; A=1; rho=1.29; dy(1,1)=y(2); dy(2,1)=-G*M/(R+y(1)).^2+.5*rho*C*A*y(2).^2/m; | function dy=gravf2(t,y); G=6.67E-11; M=5.97E24; R=6375000; m=90; C=.8; A=1; rho=1.29; dy(1,1)=y(2); dy(2,1)=-G*M/(R+y(1)).^2+.5*density(y(1))*C*A*y(2).^2/m; |
| --- | --- |
| function D=density(y) H=y*3.28084; N=length(H); for i=1:N h=H(i); if h<36152 D(i)=2116*(1.000192827-0.6864635557e-5*h)^5.256/... (8.911266*10^5-6.11608*h); elseif (h>36152 & h<82345) D(i)=0.7066418961e-3*exp(1.73-0.48e-4*h); elseif h>82345 D(i)=51.97/((.6529822044+0.4205343863e-5*h)^11.388... *(4.3748870*10^5+2.81752*h)); else D(i)=0; end end |

** Here y is in units of meters. In the next code h is in km.

% Exponential fit using fminsearch

h =  linspace(0,40,1000);

D = density(h*1000);

% Define exponential function

f = @(x,p) p(1) + p(2)*exp(-x./p(3));

% define the error function.

errf = @(p,x,y) sum((y(:)-f(x(:),p)).^2);

% an initial guess of the exponential parameters

p0 = [mean(D) (max(D)-min(D)) (max(h) - min(h))/2];

% search for solution

P = fminsearch(errf,p0,[],h,D);

% plot the result

figure(1)

plot(h,D,'k',h,f(h,P),'b-')

% Compare to linearization approach

LD=log(D);

X=h'; Y=LD';

B = [ones(length(X),1) X] \ Y;

Y2=B(2)*h+B(1);

figure(2)

semilogy(h,exp(Y2),'b')

hold

semilogy(h,D,'k')

hold

figure(3)

plot(h,density(h*1000),'k')

hold

plot(h,exp(Y2),'b')

hold

% Output function

display('Function:')

display([num2str(P(1)) ' + ' num2str(P(2)) ' exp(-x/' num2str(P(3)) ')'])

Densityfit – leads to fit:               -0.031287 + 1.3042 exp(-x/8.9719)

Attempt to use linearization before fit –

Densityfit2

Densityfit3  - using fit from last figure as compared to data

Density data based on http://www.grc.nasa.gov/WWW/k-12/rocket/atmos.html